## Slide 1
Maintenance and Reliability
Chapter 17
© 2014 Pearson Education, Inc.

## Slide 2: Outline
Global Company Profile: Orlando Utilities Commission
The Strategic Importance of Maintenance and Reliability
Reliability
Maintenance
Total Productive Maintenance

## Slide 3: Learning Objectives
When you complete this chapter you should be able to:
Describe how to improve system reliability
Determine system reliability
Determine mean time between failure (MTBF)
Distinguish between preventive and breakdown maintenance

## Slide 4: Learning Objectives
When you complete this chapter you should be able to:
Describe how to improve maintenance
Compare preventive and breakdown maintenance costs
Define autonomous maintenance

## Slide 5: Orlando Utilities Commission
Maintenance of power generating plants
Every year each plant is taken off-line for 1-3 weeks maintenance
Every three years each plant is taken off-line for 6-8 weeks for complete overhaul and turbine inspection
Each overhaul has 1,800 tasks and requires 72,000 labor hours
OUC performs over 12,000 maintenance tasks each year
© 2014 Pearson Education, Inc.

## Slide 6: Orlando Utilities Commission
Every day a plant is down costs OUC $110,000
Unexpected outages cost between $350,000 and $600,000 per day
Preventive maintenance discovered a cracked rotor blade which could have destroyed a $27 million piece of equipment
© 2014 Pearson Education, Inc.

## Slide 7: Strategic Importance of Maintenance and Reliability
The objective of maintenance and reliability is to maintain the capability of the system

## Slide 8: Strategic Importance of Maintenance and Reliability
Failure has far reaching effects on a firm’s
  Operation
  Reputation
  Profitability
  Customer satisfaction
  Reducing idle time
  Protecting investment in plant and equipment

## Slide 9: Maintenance and Reliability
Maintenance is all activities involved in keeping a system’s equipment in working order
Reliability is the probability that a machine will function properly for a specified time

## Slide 10: Important Tactics
Reliability
  Improving individual components
  Providing redundancy
Maintenance
  Implementing or improving preventive maintenance
  Increasing repair capability or speed

## Slide 11: Maintenance Management
Employee Involvement
Partnering with maintenance personnel
Skill training
Reward system
Employee empowerment
Maintenance and Reliability Procedures
Clean and lubricate
Monitor and adjust
Make minor repair
Keep computerized records
Results
Reduced inventory
Improved quality
Improved capacity
Reputation for quality
Continuous improvement
Reduced variability
Figure 17.1

## Slide 12: Reliability
System reliability
Improving individual components
Rs = R1 x R2 x R3 x … x Rn
where R1 = reliability of component 1
R2 = reliability of component 2
and so on

## Slide 13: Overall System Reliability
Reliability of the system (percent)
Average reliability of each component (percent)
| | | | | | | | |
100 99 98 97 96
100 –
80 –
60 –
40 –
20 –
0 –
n = 10
n = 1
n = 50
n = 100
n = 200
n = 300
n = 400
Figure 17.2

## Slide 14: Reliability Example
Rs
R3
.99
R2
.80
R1
.90
Reliability of the process is
Rs = R1 x R2 x R3 = .90 x .80 x .99 = .713 or 71.3%

## Slide 15: Product Failure Rate (FR)
Basic unit of measure for reliability
FR(%) = x 100%
Number of failures
Number of units tested
FR(N) =
Number of failures
Number of unit-hours of operating time
Mean time between failures
MTBF =
1
FR(N)

## Slide 16: Failure Rate Example
20 air conditioning units for use in the international space station operated for 1,000 hours
One failed after 200 hours and one after 600 hours
FR(%) = (100%) = 10%
2
20
FR(N) = = .000106 failure/unit hr
2
20,000 - 1,200
MTBF = = 9,434 hrs
1
.000106

## Slide 17: Failure Rate Example
20 air conditioning units for use in the international space station operated for 1,000 hours
One failed after 200 hours and one after 600 hours
FR(%) = (100%) = 10%
2
20
FR(N) = = .000106 failure/unit hr
2
20,000 - 1,200
MTBF = = 9,434 hrs
1
.000106
Failure rate per trip
FR = FR(N)(24 hrs)(6 days/trip)
FR = (.000106)(24)(6)
FR = .0153 failure/trip

## Slide 18: Providing Redundancy
Provide backup components to increase reliability
+
x
Probability of first component working
Probability of needing second component
Probability of second component working
RS =
(.8)
+
(.8)
x
(1 - .8)
= .8
+
.16 = .96
=

## Slide 19: Redundancy Example
A redundant process is installed to support the earlier example where Rs = .713
R1
0.90
0.90
R2
0.80
0.80
R3
0.99
RS = [.9 + .9(1 - .9)] x [.8 + .8(1 - .8)] x .99
= [.9 + (.9)(.1)] x [.8 + (.8)(.2)] x .99
= .99 x .96 x .99 = .94
Reliability has increased from
.713 to .94

## Slide 20: Parallel Redundancy
Increased reliability
through parallel
redundancy
R1
0.95
0.95
R4
0.975
R2
0.975
R3
Reliability for
the middle path
= R2 x R3 = .975 x .975 = .9506
Probability of failure
for all 3 paths
= (1 – 0.95) x (1 – .9506) x (1 – 0.95)
= (.05) x (.0494) x (.05) = .00012
Reliability of new design = 1 – .00012 = .99988

## Slide 21: Maintenance
Two types of maintenance
  Preventive maintenance – routine inspection and servicing to keep facilities in good repair
  Breakdown maintenance – emergency or priority repairs on failed equipment

## Slide 22: Implementing Preventive Maintenance
Need to know when a system requires service or is likely to fail
High initial failure rates are known as infant mortality
Once a product settles in, MTBF generally follows a normal distribution
Good reporting and record keeping can aid the decision on when preventive maintenance should be performed

## Slide 23: Computerized Maintenance System
Figure 17.3
Output Reports
Inventory and purchasing reports
Equipment parts list
Equipment
history reports
Cost analysis
(Actual vs. standard)
Work orders
Data Files
Personnel data with skills, wages, etc.
Equipment file with parts list
Maintenance
and work order schedule
Inventory of spare parts
Repair history file

## Slide 24: Maintenance Costs
The traditional view attempted to balance preventive and breakdown maintenance costs
Typically this approach failed to consider the full costs of a breakdown
  Inventory
  Employee morale
  Schedule unreliability

## Slide 25: Maintenance Costs
Figure 17.4 (a)
Total costs
Breakdown maintenance costs
Costs
Maintenance commitment
Traditional View
Preventive maintenance costs
Optimal point (lowest
cost maintenance policy)

## Slide 26: Maintenance Costs
Figure 17.4 (b)
Costs
Maintenance commitment
Full Cost View
Optimal point (lowest
cost maintenance policy)
Total costs
Full cost of breakdowns
Preventive maintenance costs

## Slide 27: Maintenance Cost Example
Should the firm contract for maintenance on their printers?
NUMBER OF BREAKDOWNS | NUMBER OF MONTHS THAT BREAKDOWNS OCCURRED |  | 
0 |  | 2 | 
1 |  | 8 | 
2 |  | 6 | 
3 |  | 4 | 
 | Total : | 20 | 
Average cost of breakdown = $300

## Slide 28: Maintenance Cost Example
Compute the expected number of breakdowns
NUMBER OF BREAKDOWNS | FREQUENCY | NUMBER OF BREAKDOWNS | FREQUENCY
0 | 2/20 = .1 | 2 | 6/20 = .3
1 | 8/20 = .4 | 3 | 4/20 = .2
∑
Number of breakdowns
Expected number of breakdowns
Corresponding frequency
=
x
= (0)(.1) + (1)(.4) + (2)(.3) + (3)(.2)
= 0 + .4 + .6 + .6
= 1.6 breakdowns / month

## Slide 29: Maintenance Cost Example
Compute the expected breakdown cost per month with no preventive maintenance
Expected breakdown cost
Expected number of breakdowns
Cost per breakdown
=
x
= (1.6)($300)
= $480 per month

## Slide 30: Maintenance Cost Example
Compute the cost of preventive maintenance
Preventive maintenance cost
Cost of expected breakdowns if service contract signed
Cost of
service contract
=
+
= (1 breakdown / month)($300) + $150 / month
= $450 / month
Hire the service firm; it is less expensive

## Slide 31: Increasing Repair Capabilities
Well-trained personnel
Adequate resources
Ability to establish repair plan and priorities
Ability and authority to do material planning
Ability to identify the cause of breakdowns
Ability to design ways to extend MTBF

## Slide 32: Increasing Repair Capabilities
Figure 17.5
Operator
(autonomous maintenance)
Maintenance department
Manufacturer’s field service
Depot service
(return equipment)
Increasing Operator Ownership
Increasing Complexity
Preventive
maintenance costs less and
is faster the more we move to the left
Competence is higher as we
move to the right

## Slide 33: Autonomous Maintenance
Employees accept responsibility for
  Observe
  Check
  Adjust
  Clean
  Notify
Predict failures, prevent breakdowns, prolong equipment life

## Slide 34: Total Productive Maintenance (TPM)
Designing machines that are reliable, easy to operate, and easy to maintain
Emphasizing total cost of ownership when purchasing machines, so that service and maintenance are included in the cost

## Slide 35: Total Productive Maintenance (TPM)
Developing preventive maintenance plans that utilize the best practices of operators, maintenance departments, and depot service
Training for autonomous maintenance so operators maintain their own machines and partner with maintenance personnel

## Slide 36: More on Maintenance –
A simple redundancy formula
Problems with breakdown and preventive maintenance
Predictive maintenance
Predictive maintenance tools
Maintenance strategy implementation
Effective reliability
Supplemental Material

## Slide 37: Providing Redundancy – An Alternate Formula
The reliability of one pump = The probability of one pump not failing = 0.8
P(failing) = 1- P(not failing) = 1 - 0.8 = .2
P(failure of both pumps) =
P(failure) pump #1 x P(failure) pump #2
P(failure of both pumps) = 0.2 x 0.2 = .04
P(at least one pump working) =
1.0 - .04 = .96
If there are two pumps with the same probability of not failing
Notes: 37

## Slide 38: Problems With Breakdown Maintenance
Run it till it breaks”
  Might be ok for low criticality equipment or redundant systems
  Could be disastrous for mission-critical plant machinery or equipment
  Not permissible for systems that could imperil life or limb (like aircraft)
Notes: 38

## Slide 39: Problems With Preventive Maintenance
Fix it “whether or not it is broken”
  Scheduled replacement or adjustment of parts/equipment with a well-established service life
  Typical example – plant relamping
  Sometimes misapplied
    Replacing old but still good bearings
    Over-tightening electrical lugs in switchgear
Notes: 39

## Slide 40: Another Maintenance Strategy
Predictive maintenance – Using advanced technology to monitor equipment and predict failures
  Using technology to detect and predict imminent equipment failure
  Visual inspection and/or scheduled measurements of vibration, temperature, oil and water quality
  Measurements are compared to a “healthy” baseline
  Equipment that is trending towards failure can be scheduled for repair
Notes: 40

## Slide 41: Predictive Maintenance Tools
Vibration analysis
Infrared Thermography
Oil and Water Analysis
Other Tools:
  Ultrasonic testing
  Liquid Penetrant Dye testing
  Shock Pulse Measurement (SPM)
Notes: 41

## Slide 42: Predictive Maintenance Vibration Analysis
Using sensitive transducers and instruments to detect and analyze vibration
Typically used on expensive, mission-critical equipment–large turbines, motors, engines or gearboxes
Sophisticated frequency (FFT) analysis can pinpoint the exact moving part that is worn or defective
Can utilize a monitoring service
Notes: 42

## Slide 43: Predictive Maintenance Infrared (IR) Thermography
Using IR cameras to look for temperature “hot spots” on equipment
Typically used to check electrical equipment for wiring problems or poor/loose connections
Can also be used to look for “cold (wet) spots” when inspecting roofs for leaks
High quality IR cameras are expensive – most pay for IR thermography services
Notes: 43

## Slide 44: Predictive Maintenance Oil and Water Analysis
Taking oil samples from large gearboxes, compressors or turbines for chemical and particle analysis
    Particle size can indicate abnormal wear
Taking cooling water samples for analysis – can detect excessive rust, acidity, or microbiological fouling
Services usually provided by oil vendors and water treatment companies
Notes: 44

## Slide 45: Predictive Maintenance Other Tools and Techniques
Ultrasonic and dye testing – used to find stress cracks in tubes, turbine blades and load bearing structures
    Ultrasonic waves sent through metal
    Surface coated with red dye, then cleaned off, dye shows cracks
Shock-pulse testing – a specialized form of vibration analysis used to detect flaws in ball or roller bearings at high frequency (32kHz)
Notes: 45

## Slide 46: Maintenance Strategy Comparison
MAINTENANCE STRATEGY | ADVANTAGES | DISADVANTAGES | RESOURCES/ TECHNOLOGY REQUIRED | APPLICATION EXAMPLE
Breakdown | No prior work required | Disruption of production, injury or death | May need labor/parts at odd hours | Office copier
Preventive | Work can be scheduled | Labor cost, may replace healthy components | Need to obtain labor/parts for repairs | Plant relamping, machine lubrication
Predictive | Impending failures can be detected & work scheduled | Labor costs, costs for detection equipment and services | Vibration, IR analysis equipment or purchased services | Vibration and oil analysis of a large gearbox
Notes: 46

## Slide 47: Maintenance Strategy Implementation
Breakdown
Preventive
Predictive
1 2 3 4 5 6 7 8 9 10
Year
100%
80%
60%
40%
20%
0%
Percentage of Maintenance Time by Strategy
Notes: 47

## Slide 48: Is Predictive Maintenance Cost Effective?
In most industries the average rate of return is 7:1 to 35:1 for each predictive maintenance dollar spent
Vibration analysis, IR thermography and oil/water analysis are all economically proven technologies
The real savings is the avoidance of manufacturing downtime – especially crucial in JIT

## Slide 49: Predictive Maintenance and Effective Reliability
Effective Reliability (Reff) is an extension of Reliability that includes the probability of failure times the probability of not detecting imminent failure
Having the ability to detect imminent failures allows us to plan maintenance for the component in failure mode, thus avoiding the cost of an unplanned breakdown
Reff = 1 – (P(failure) x P(not detecting failure))
Notes: 49

## Slide 50: How Predictive Maintenance Improves Effective Reliability
Example: a large gearbox with a reliability of .90 has vibration transducers installed for vibration monitoring. The probability of early detection of a failure is .70. What is the effective reliability of the gearbox?
Reff = 1 – (P(failure) x P(not detecting failure))
Reff = 1 – (.10 x .30) = 1 - .03 = .97
Vibration monitoring has increased the effective reliability from .90 to .97!
Notes: 50

## Slide 51: Effective Reliability Caveats
Predictive maintenance only increases effective reliability if:
    You select the method that can detect the most likely failure mode
    You monitor frequently enough to have high likelihood of detecting a change in component behavior before failure
    Timely action is taken to fix the issue and forestall the failure (in other words you don’t ignore the warning!)
Notes: 51

## Slide 52: Increasing Repair Capabilities
Well-trained personnel
Adequate resources
Proper application of the three maintenance strategies
Continual improvement to improve equipment/system reliability
Notes: 52